- If your skin has a resistance of 100,000 ohms, and you touch a 9-volt battery, what current will flow through you?

- A light bulb draws 0.5 amps of current on a 9-volt battery. What is the resistance in the circuit?

- How much resistance is in a toaster that draws 5 amps of current when plugged into a 110-volt wall socket?

- How much resistance is in a light bulb that draws 0.3 amps of current when attached to a 1.5-volt "D" battery?

- What voltage is needed to run an electric iron drawing 5.5 amps of current through a circuit with a resistance of 20 ?